Fifteen Years of Acoustic Data from MDI
Tim Larson
Stanford University
tplarson@sun.stanford.edu

---
dopplergrams
remap to regular
grid in longitude,
sin(latitude)
fourier transform
 in longitude
calculate plm’s
and project onto
spherical harmonics
retile to desired
length in time
and chunking in l
detrend and
fill gaps
generate fourier
transforms and/or
power spectra
time
series
time
series
output
output
peakbagging/
ridge fitting
inversions for
internal rotation
and sound speed
    mode
parameters
profiles
leakage
matrix

---
Dataseries
mdi.vw_V_sht_72d
mdi.vw_V_sht_secs
mdi.vw_V_sht_gaps_72d
mdi.vw_V_sht_gf_72d
mdi.vw_V_sht_gf_gaps_72d
mdi.vw_V_sht_gf_gaps_retile
mdi.vw_V_sht_pow
mdi.vw_V_modes
mdi.vw_V_modes_asym

---
Keywords
T_START – the beginning of the time interval a record corresponds to. This will always be the first primekey of these dataseries. It can be specified as a date string or as an offset from the MDI epoch 1993.01.01_TAI.
LMIN – minimum spherical harmonic degree represented.
LMAX – maximum spherical harmonic degree represented.
NDT – number of time points represented.
T_STEP – length of a time step in seconds, usually a constant. The length of the timeseries is then NDT times T_STEP.
T_STOP – the beginning of the following timeseries, or T_START + NDT * T_STEP.
T_OBS – the midpoint of a timeseries as given by (T_START + T_STOP) / 2.
VERSION – string describing the version of the data, updated whenever reprocessing occurs, useful for recovering obsolete versions of records.
LMIN and LMAX will be the second and third primekeys when applicable.
NDT will be the last primekey when applicable.

---
Sonification
What I've tried so far...
- Use mode parameters to filter data in frequency domain, inverse transform, take real part.
- Speed up by a factor of 60000 (arbitrary), 72 days → ~100 seconds, 3 mHz →180 Hz
- Implies sample rate of 1 kHz, turns out most audio players refuse to play this.
- Shift filtered fft's down by a factor of 8, inverse transform, sample at 8 kHz, same frequency content plays in ~13 seconds.
- Use SoX (Sound eXchange) utility to mix, change sample rate and tempo as needed.